## Slide 1: Graduation project
GPS module

## Slide 2: GPS in WAP
the phasor, and, in particular, its phase-angle, is calculated using Coordinated Universal Time (UTC) as a time reference.
Such choice allows having a unique reference for all the sinusoidal signals to be measured in a wide or global area, because the time dissemination relies on satellite systems.

## Slide 3: GPS in WAP
Two synchrophasors, calculated at different points in a network, can be easily compared because they are related to common instants.
In other words, the synchrophasor measured at a generic UTC reference time instant “Tr “represents the rms amplitude and the phase-angle of the sinusoidal signal at T .

## Slide 4: GPS module”SKM55RM”

## Slide 5: GPS module”SKM55RM”

## Slide 6: GPS module”SKM55RM”

## Slide 7: Hardware Interfaces Configuration
UART Ports:
The SKM55 series supports one full duplex serial channels UART.
The serial connections are at 2.85V LVTTL logic levels, if need different voltage levels, use appropriate level shifters. the data format is however fixed: X, N, 8, 1, i.e. X baud rate, no parity, eight data bits and one stop bit, no other data formats are supported, LSB is sent first. The modules default baud
rate is set up 9600bps.

## Slide 8: Hardware Interfaces Configuration
RS232 Ports:
The SKM55 series uses single-chip RS232 to UART bridge, It is 3V powered EIA/TIA-232 and V.28/V.24 communication interfaces with low power requirements.

## Slide 9: Hardware Interfaces Configuration

## Slide 10: RS232 protocol to TTL protocol
*Using max232 IC as logic shifter.

## Slide 11: MAX232 connection
Using Atmega 128 instead of Arduino in our case.

## Slide 12: Software Protocol
NMEA 0183 Protocol :
The NMEA protocol is an ASCII-based protocol,
records start with a “$ “and with carriage return/line feed.
GPS specific messages all start with $GPxxx where xxx
is a three-letter identifier of the message data that
follows.
NMEA messages have a checksum, which allows detection of corrupted data transfers.

## Slide 13: Software Protocol
NMEA Record Description
GGA Global positioning system fixed data.
GLL Geographic position-latitude/longitude.
GSA GNSS DOP and active satellites.
GSV GNSS satellites in view .
RMC Recommended minimum specific
GNSS data .
VTG Course over ground and ground speed.
ZDA Date and Time

## Slide 14: Software Protocol
GGA-Global Positioning System Fixed Data :
“$GPGGA,021514.000,2232.1799,N,11401.1823,E,1,6,1.25,84.0,M,-2.2,M,,*74 “.
This sentence contains the position, time and quality of the navigation fix.
“Nema protocol,UTC,Latitude,N,Longitude,E,PF,......”

## Slide 16: Software layers

## Slide 17: Software layers

## Slide 18: Software code using embedded C

## Slide 19: Software code using embedded C

## Slide 20: Software code using embedded C

## Slide 21: Software code using embedded C

## Slide 22: Software code using embedded C

## Slide 23: Software code using embedded C

## Slide 24: Software code using embedded C

## Slide 27: Graduation project
HMI modules

## Slide 28: LCD LM016

## Slide 29: LCD LM016

## Slide 30: LCD LM016

## Slide 31: LCD LM016

## Slide 32: LCD LM016

## Slide 33: LCD LM016

## Slide 34: LCD LM016

## Slide 35: LCD LM016

## Slide 36: LCD LM016

## Slide 37: LCD LM016

## Slide 38: LCD LM016

## Slide 39: LCD LM016

## Slide 40: LCD LM016

## Slide 41: LCD LM016

## Slide 42
SMART TOUCH LCD

## Slide 43: SMART TOUCH LCD

## Slide 44: SMART TOUCH LCD

## Slide 45: SMART TOUCH LCD

## Slide 46: SMART TOUCH LCD

## Slide 47: SMART TOUCH LCD

## Slide 48: SMART TOUCH LCD

## Slide 49: SMART TOUCH LCD

## Slide 50: SMART TOUCH LCD

## Slide 51: SMART TOUCH LCD

## Slide 52: Embedded C programing code

## Slide 53: Embedded C programing code

## Slide 54
The End.