## Slide 1: Graduation Project (Final Discussion)

## Slide 2: Wide Area Protection :
INTRODUCTION :
The growth of electrical power systems is a challenge for Energy Management Systems to ensure a safe and reliable operation, This situation originates the need for tools that help to visualize and control electrical system variables using high speed communications channels and accurate data, allowing the grid operator to estimate the state of the system in real time through mathematical calculations,, We can define Wide Area Systems as a Summation of small or large areas that are not connected directly to each other and are separated from each other and it have a large distance between each other and through Wide Area Protection system Real- Time data can be collected from all these Areas and then it can be shared to each other and then monitored at one place and then controlling the whole Area from the Control Station.

## Slide 3
There are many defects in the traditional Protection schemes so we used the Wide Area Protection as a Back-up Protection and these reasons are as follow :
1- Modern power systems are in the process of continuous development which has led to complex interconnected Networks, Financial pressure on the electricity market and on grid operators forces them to maximize the utilization of high voltage equipment, which very often lead their operation closer to the limits of the system, This approach of ensuring economic operation is possible provided the system is equipped with a well-designed and coordinated protection and control strategy to deal with wide spread disturbances in the system.

## Slide 4
2-Traditional power system protection and control measures are based on local measurements, However, it is quite difficult to maintain the stability and security of the system on the whole, if only local measurements are employed in the protection and control schemes,, One promising way is to provide a system wide protection and control, complementary to the conventional local protection strategies, While it is not possible to predict or prevent all contingencies that may lead to power system collapse, a wide-area monitoring and control system that provides a reliable security prediction and optimized coordinated action is able to mitigate or prevent large area disturbances, The main tasks, which can be accomplished through wide-area based monitoring and control.

## Slide 5
3- Conventional Problems happened because of many things like false tripping or not tripping at all and all of these problems can cause at some times serious problems that may lead to disasters and these problems should be controlled and isolated once it happened and for example,, The distance relays which are widely used in the protection nowadays and it involve the determination of impedance achieve operating times of the order of a period of the power system frequency, A distance relay is designed to only operate for faults occurring between the relay location and the selected reach point, and remains stable for all faults outside this region or zone, Consider that a fault with a resistance happened to this zone of the Distance Relay then what will happen?
The resistance of the fault arc takes the fault impedance outside the relay’s tripping characteristic and, hence, it does not detect this condition. Alternatively, it is only picked up either by zone 2 or zone 3 in which case tripping will be unacceptably delayed, The distance relays are based on standalone decision, while each relay operates independently according to three different zone of operation.

## Slide 6: Wide Area Protection as a Back-up Protection :
Wide-area protection and its development : WAPS are focused on two fields: First is security, stability and control, Second is the relay protection, In the security and stability control field,, WAPS is mainly used to prevent long-term voltage collapse It is established on basis of the supervisory control and data acquisition (SCADA) system, with centralized decision-making structures, non-real-time data collection, and slow data refresh frequency, The communication system does not require fast, real-time data exchange,, Compared to the traditional strategies of stability control, WAPS involves a wider geographical scope and requires more complex calculations in the processes of getting information, forming control strategies, and carrying out control measures.

## Slide 7
In the relay protection field, It uses globe positioning system (GPS) signals for precise time synchronization with using PMU devices and then collect all these data from these Devices and send it to PDC, and a dedicated fiber channel for multi-point current information transmission, And it can be easily make a backup protection for the system and avoid traditional problems.

## Slide 8
The communication of data among them is carried via optic-fiber networks, The relay decision is based on collected and shared data through communication network. The suggested technique satisfies high degree of reliability and stability while it is based on shared decision rather than standalone decision. The suggested technique can see all the power system area and can deal with the transmission lines as unit protection.

## Slide 9
While Traditional protection relays and devices operate through slow times, and these actions are certainly uncoordinated, Coordinated actions will be taken through SCADA/EMS systems by operators, however in prolonged times, which might make the situations too late to rescue,, Wide Area Protection (WAP) systems provide a very promising future in the face of wide-area disturbances and blackouts,, Phasor measurement technologies now allow accurate comparison of measurements over widely separated locations as well as potential real-time measurement based control actions. Hence WAP systems could be employed to fulfill the two main objectives of increasing transmission capability as well as increasing system reliability, by performing a real-time, look ahead analysis giving some recommendation of possible updated control strategies and actions, especially in the events of contingencies. The WAP system shall know what actions to take based on the present system condition in the case that a certain contingency occurring, or would take an action saving the system progressing into an unstable state.

## Slide 10
The Wide Area protection and control are exist at bay, substation and regional levels, Covering both transmission and distribution networks, the system is supported by the proposed high speed synchronized communication network and the real-time protection and control information platform, The system section techniques and the latest developments in control system, offers not only fast protection, but also complete control of entire power network.

## Slide 11: Wide Area Monitoring is the first step of Wide Area Protection:
The Wide Area Monitoring System (WAMS) consists of geographically dispersed Phasor Measurement Units (PMUs) delivering Synchrophasors, i.e., time-tagged data samples of a power system’s sinusoidal voltage or current using a standard time signal as the reference, to Phasor Data Concentrators (PDCs), These (PDCs) perform the desired signal handling and assembly of synchronized Phasor measurements into snapshots. They may also facilitate long term storage in high-resolution historical archives. The data in each PMU are time Synchronized to Universal Coordinated Time (UTC),, (WAM) became one of the most recent technologies that are popular for upgrading the traditional electric grid, This upgrade has become a necessity to modernize the electricity delivery system following the occurrence of major blackouts in power systems around the world

## Slide 12
Wide Area Monitoring Systems collect the information from the power system, analyze the data and interpret the result, giving “warnings” to the system operator or initiating “defense schemes” in order to prevent stability problems,, WAMS consist of the 3 major components: Phasor Measurement Unit (PMU), Phasor Data Concentrator (PDC) and communication channel.

## Slide 13: Applying Wide Area Protection as a back-up
Protection for the whole system :
Blackouts and load shedding are major problems faced in the current world. These can be avoided by properly monitoring and controlling the existing power grid. Proper monitoring and controlling of power grid can be done using a PMU, The parameters measured using PMUs can be transmitted throughout the network, Smart grid is a modernized power grid that uses digital processing and communication technology to detect and react to local changes in the network thus providing stable and quality power at affordable rates.

## Slide 14
Thus fault detection is improved and allows self-healing using state estimation, The information from the grid must be obtained in a synchronized manner in order to ensure uniform distribution of power over a large area. PMUs are installed throughout the transmission side of the grid and these monitor the state of the electrical network. These networks of PMUs are called WAMS, These PMUs are time synchronized using GPS. PMUs provide phasor parameters of the signal. It monitors the status of the switches, status of the circuit breakers, equipment performance, congestion, outages and demand response events, At first implementing the PMUs at the System with an algorithm of using PMUs at 25% of the number of the existed buses at the whole system.

## Slide 15: Conventional protection schemes and a wide-
area backup protection system :
According to recent studies, the mal-operation or fail-to trip of protection is determined as one of the origins to raise and propagate major power system disturbances. A vast majority of relay mal- operations are unwanted trips and have been shown to propagate major disturbances. A CIGRE study found that 27% of bulk power system disturbances resulted from false trips of the protection system. The major reason of these conventional solutions lies in that local protection devices are not considering a system view and are therefore not able to take optimized and coordinated actions. Backup protections in fault clearance system have the task to operate only when the primary protection fails to operate or when the primary protection is temporarily out of service. The recent complexity and enlargement of power systems makes it difficult to coordinate operation times and reaches among relays

## Slide 16
Especially, In the existed relay protection system, mal operations of backup protection contribute a lot to system security and stability; furthermore, they are main reasons to system cascade tripping, To solve this problem, one proposal is to add an intelligent analyzing and controlling function in key process of protection functionality, In the areas of power system automation and substation automation, there are two different trends: centralization and decentralization. More and more dynamic functions are moving from local and regional control centers toward central or national control centers. At the same time we also observe more "intelligence" and "decision power" moving closer towards the actual power system substations. Greater functional integration is being enclosed in substation hardware. In view of global security of power systems, the action algorithms of conventional backup protections possibly are not best choices because the operations of individual relays are hardly coordinated each other.
Therefore, the principle of the protection design needs innovation to overcome the above problem.

## Slide 17
The proposed system comprises a master system and several local units. The system is arranged as three layers. The bottom layer consists of PMUs with additional protection functionality. The next layer consists of several Local Backup Protection Centers (LBPCs), each of which interfaces directly with a number of PMUs. The top layer, System Backup Protection Center (SBPC), acts as the coordinator for the LBPCs. Connected together via fiber-optic communication links.

## Slide 18
The proposed system comprises a master system and several local units. The system is arranged as three layers. The bottom layer consists of PMUs with additional protection functionality. The next layer consists of several Local Backup Protection Centers (LBPCs), each of which interfaces directly with a number of PMUs. The top layer, System Backup Protection Center (SBPC), acts as the coordinator for the LBPCs.
Connected together via fiber-optic communication links, these devices
can process intelligent algorithms based on data collected locally, Local part of the proposed wide-area backup system comprises PMUs and LBPC, which are both installed in the station, PMUs are made up of DSP (Digital Signal Processor) and GPS(Global Positioning System). The DSP measures instantaneous voltages and currents of protected power system in real-time, and calculates the state variables, which provide vital information for backup protection system.

## Slide 19
Then, power system variable data is transferred to LBPC, LBPC samples digital inputs, and pre-processes the analog and digital signals, and then deliver preprocessed results to SBPC via fiber-optic communications between the substation and SBPC. SBPC will be installed at Regional Control Center, and integrates various well- developed functions, such as data acquisition via communication, system monitoring, fault location, security analyzing, making tripping strategy and descending strategy to LBPCs, also, SBPC can do post- event playback and post-event data analyses. These functions employ PMUs to fulfill real-time demand,, LBPCs perform the correlative operations on the spot when receiving the strategy from SBPC, then fault will be isolated rationally. While it is not possible to prevent all contingencies that may lead to power system collapse, a wide area backup protection system that provides a reliable security isolated scheme and optimized coordinated actions is able to mitigate or prevent large area disturbances.